THE TINY PRO BOARD

Feature：

The smallest size

The latest DC module

One IMU On board

SPEK INTERFACE

The Max current 2.5A/each motor

SH1.0 encoder interface （PWM)

SIZE:  54x25mm

Details：

Current: The drive of the motor use DRV8313

(the same as BaseCam regular board S-BGC)，

continuous current 1.75A for each motor, the

Max current 2.5A for each motor

Voltage: Used the latest DC module, the Max

voltage can up to 40V,(Recommend the use of

6S battery), We used the latest High current

3.3V module, it will more Safety when you use

External equipment.

Motor interface:

optimize for high current demand

and same method like S-BGC.

The IMU on board:

it have a master-slave jumper

settings, You can use it for Frame or Camera

Just need cut the jump as the picture,you can get the

Frame IMU

SPEK INTERFACE:

Support Spectrum Satellite receiver (same function as S-BGC)

J2 and J3 jumper：

Used Basecam newest I2C-Drive hardware design

and can ensure tiny pro can work more stable

SH1.0 Encoder interface(PWM) :

Special independent

Multiplexing encoder interface ,

easier to wire compare with

Other board in the market

RC interface :

Same circuit layout as basecam

tiny board ,maxiumize to reduce

board size.

Series interface :

More stable when connect with PC than

standard  tiny board cause we used

CP2102 chip(same as S-BGC) but

tiny board applied ST simulate interface .

The CNC enclosure :